FIRE PREVENTION AND CONTROL QUIZ #1

- Small quantities of flammable liquids stored in safety cans do not need to be labeled as to contents.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Onsite fire fighting equipment shall be ___________ that can extinguish fires of any class that could occur as a result of hazards present.

|  | a. The type |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. The size |  |  |  |
|  | c. The quantity |  |  |  |
|  | d. All of the above |  |  |  |

- Dry chemical fire extinguishers with mild steel shells are required to be hydrostatic tested every _____ years.

|  | a. Five |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Six |  |  |  |
|  | c. Ten |  |  |  |
|  | d. Twelve |  |  |  |

- Be sure to close valves on oxygen and acetylene cylinders to prevent accidental release of gases from hoses and torches when –

|  | a. Cylinders are moved |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Torch and hoses are left unattended |  |  |  |
|  | c. Task is completed |  |  |  |
|  | d. All of the above |  |  |  |

- A multi-purpose dry chemical fire extinguisher must have a rating of –

|  | a. 4-A:10B:C |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. 2-A:10B:C |  |  |  |
|  | c. Contains a nominal 2.5 lbs. of dry chemical agent |  |  |  |
|  | d. Contains a nominal 4.5 lbs. or more of dry chemical agent |  |  |  |
|  | e. B and D |  |  |  |

- Maintenance checks of fire extinguishers are required once every twelve months.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Oxygen cylinders must not be stored together in rooms or areas with flammable or combustible liquids.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Fire extinguishers are required to be visually inspected at least ___________ to determine that they are fully charged and operable.

|  | a. Once a week |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. Once a month |  |  |  |
|  | c. Quarterly |  |  |  |
|  | d. None of the above |  |  |  |

- Fire hydrants that are a part of the fire fighting system must be visually inspected at least once every three months for damage and deterioration and use-tested at least once every twelve months to determine that they remain functional.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Signs prohibiting smoking and open flames are to be posted where a fire or explosion hazard exists.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- You can use flammable liquids such as gasoline for cleaning purposes.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Battery charging stations are required to be ventilated to prevent the build up of hydrogen gas.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

# Signature ________________________________ Payroll # _____________ Date __________________

Instructor _________________________________ Instructor __________________________________