HAND AND PORTABLE POWERED TOOLS QUIZ #1

Answers

- Never point a compressed air gun towards anyone or use it to blow dust off your clothing.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Before installing a new abrasive wheel on a portable hand-held grinder, you are required to –

|  | a. inspect wheel for cracks and damage. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. check RPM rating to ensure it is right for the grinder. |  |  |  |
|  | c. perform a “ring test” to determine if the wheel is cracked. |  |  |  |
|  | d. all of the above. |  |  |  |

- You should never carry a power tool by its cord because it may pull apart creating an electrical hazard.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- All hand and portable powered tools must be inspected prior to use.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Guards on portable powered tools are provided to protect the user and other people from –

|  | a. point of operation hazards. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. in-running nip point hazards. |  |  |  |
|  | c. rotating parts. |  |  |  |
|  | d. flying chips and sparks hazards. |  |  |  |
|  | e. all of the above. |  |  |  |

- Two hand tool hazards are using a screwdriver as a chisel and using a chisel with a mushroomed head.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- The user’s manual supplied by the manufacturer provides valuable information on inspection procedures, operating procedures, and maintenance requirements.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Hose connections for pneumatic powered hand tools must have a positive locking device such as a safety clip to prevent separation of hoses.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Power tools must be disconnected from the power source when –

|  | a. not in use. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. changing accessories. |  |  |  |
|  | c. servicing. |  |  |  |
|  | d. all of the above. |  |  |  |

- Basic safety rules for hand and portable powered tools include –

|  | a. keeping tools in good condition. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. performing regular maintenance. |  |  |  |
|  | c. using the right tool for the job. |  |  |  |
|  | d. examining for damage before use. |  |  |  |
|  | e. operating according to manufacturer’s instructions. |  |  |  |
|  | f. wearing proper PPE. |  |  |  |
|  | g. all of the above. |  |  |  |

- Never remove a safety guard when using a hand or portable powered tool.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Electrical powered portable tools can be double insulated.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Powder-actuated powered hand tools operate like a loaded gun so treat them with respect and follow all precautions recommended by the manufacturer.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- Hand-held powered tools must be equipped with a constant pressure switch that will shut off the power when the pressure is released.

|  | a. True |  | b. False |  |
| --- | --- | --- | --- | --- |

- When using a jack, be sure –

|  | a. the base is resting on a firm level surface. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. it is correctly centered. |  |  |  |
|  | c. the jack head bears against level surface. |  |  |  |
|  | d. the lift force is applied evenly. |  |  |  |
|  | e. all of the above. |  |  |  |

- The safe condition of hand tools used on-the-job is the responsibility of –

|  | a. the employee. |  |  |  |
| --- | --- | --- | --- | --- |
|  | b. the employer. |  |  |  |
|  | c. both a and b. |  |  |  |
|  | d. the manufacturer. |  |  |  |

# Signature __________________________________ PR # ___________ Date ______________________

Instructor _______________________________ Instructor ____________________________________