As an agent of the company you should be familiar with the following 30 CFR standards and sections of the ACT.

Objective:  To familiarize all levels of supervision in mine law and governing 30 CFR standards.

Time:  approximately 2 hours

1.  Safety rules and _____________shall be taught to __________________.

Standard number(s) .18006

Answer:  safe work procedures-----new employees

2.  When should fire extinguishers be placed on mobile equipment?

Standard number(s)  .4230

Answer:  whenever a fire or its effects could impede escape

3.  Spillage of _________________or________________ shall be removed in ______________.

Standard number(s) .4102

Answer:  flammable or combustible liquids------- a timely manner

4.  Unguarded conveyors next to travelways shall be equipped with __________or ____________.

Standard number(s) .14109

Answer:  emergency stop devices---or railings

5.  What is the definition of a competent person?

Standard number(s) definitions—subpart A

Answer:  a person having abilities and experience that fully qualify him to perform the duty to which he is assigned

6.  What should be done with waste or rags that have combustible material on them?

Standard number(s) .4104

Answer:  placed in covered metal containers or other equivalent containers with flame containment characteristics

7.  Fixed ladders shall project ____________ above landings or have ______________________.

Standard number(s) .11006

Answer:  at least 3 feet------substantial handholds provided above the landing

8.  What shall be done to snow & ice on walkways & travel ways & when shall it be done?

Standard number(s) .11016

Answer:  sanded, salted, or cleared as soon as practicable

9.  When shall lights be guarded?

Standard number(s) .12034

Answer:  that by their location presents a shock or burn hazard

10.  What is required for barricades and warning signs where hazards exist?

Standard number(s) .20011

Answer:  posted at all approaches—signs shall be readily visible, legible & display the nature of the hazard & protective action required

11.  What shall be used on high pressure hoes connections with inside diameter of __________or larger?

Standard number(s) .13021

Answer:  safety chains or other suitable locking devices shall be used on ¾ inch inside diameter or larger

12.   What is required when working with suspended loads?

Standard number(s) .16009

Answer:  stay clear

13.  What is the definition of a travel way?

Standard number(s) Subpart A General

Answer: a passage, walk or way regularly used & designated for persons to go from one place to another

14. Machinery, equipment and tools cannot be used in what way?

Standard number(s) .14205

Answer:  beyond the design capacity intended by the manufacturer where such use may create a hazard to persons

15.  When should fire extinguishers be replaced?

Standard number(s) .4203

Answer:  promptly after any discharge

16.  Oxygen cylinders cannot be stored where?

Standard number(s) .4601

Answer:  in rooms or areas used or designated for storage of flammable or combustible liquids, including grease

17.  How should guards be constructed and maintained?

Standard number(s) .14112(a)(1)

Answer:  to withstand the vibration, shock, & wear to which they will be subjected during normal operations

18.  When shall welding operations be shielded?

Standard number(s) .14213

Answer:  where arc flash could be hazardous to persons

19.  What must be done when operating equipment around high voltage power lines?

Standard number(s) .12071

Answer:  work 10 ft. or more from the lines or the lines shall be deenergized or other precautionary measures taken

20.  How many feet must flammable or combustible material be away from electrical substations?

Standard number(s) .4130

Answer:  25 feet

21.  What are waste receptacles used for and how are they to be maintained?

Standard number(s) .20013

Answer:  disposal of waste food & associated material emptied frequently & maintained in a clean & sanitary condition

22.  When should emergency medical assistance & transportation be arranged?

Standard number(s) .18014

Answer:  made in advance

23.  What is the definition of high potential?

Standard number(s) Subpart A General

Answer: more than 650 volts

24.  Where shall emergency phone numbers be posted?

Standard number(s) .18012

Answer:  shall be posted at appropriate telephones

25.  What are the use restrictions for flammable liquids?

Standard number(s) .4400(a)

Answer:  shall not be used for cleaning

26.  Who shall be designated the person in charge and what is that person’s responsibility?

Standard number(s) .18009

Answer:  a competent person designated by the mine operator-to take charge in case of an emergency

27.  When shall machinery not be lubricated?

Standard number(s) .14204

Answer:  while it is in motion where application may expose persons to injury

28.  Where shall proper illumination (light) be provided?

Standard number(s) .17001

Answer:  on all surface structures, paths, walkways, stairways, switch panels, loading & dumping sites & work areas

29.  How far shall material be removed from the top of the pit or quarry wall?

Standard number(s) .3131

Answer:  at least 10 feet

30.  What is the definition of a misfire?

Standard number(s) Subpart A General

Answer:  the complete or partial failure of a blasting charge to explode as planned

31.  What are the parking procedures for unattended equipment?

Standard number(s) .14207

Answer:  controls are in the park position-parking brakes are set-on a slope wheels or tracks are choked or turned into a bank

32.  How should ladders be constructed and maintained?

Standard number(s) .11003

Answer:  substantial construction & maintained in good condition.

33.  Persons shall not be transported in what?

Standard number(s) .9200(a)(b)(c)(d)(e)

Answer:  dippers, forks, clamshells, buckets, beds of mobile eq., on top of loads, outside cabs, between cars of trains, leading end of trains, over crowded mobile eq., in mobile eq. with materials or eq. unless the items are secured, on conveyors

34.  How long before a person can enter a blast area when a misfire is suspected?

Standard number(s): .6310

Answer:  for 30 mins. If safety fuse & blasting caps are used-for 15 mins. If other type of detonators are used

35.  How should power conductors be protected from moving equipment?

Standard number(s) .12005

Answer:  properly bridged or protected