Blasting Safety- Questions for non-blasters

General Safety

- Undetonated explosives are easy for anyone to identify. True / False

- A written blasting plan is required for using explosives. True / False

Explosives Storage

- An explosives magazine may be located near which of the following? a) power lines, b) fuel storage areas, c) damp, moisture laden areas, d) heavily populated areas, e) None of the above.

- Explosive magazines should not be identifiable as such to the general public. (True/ False)

- Explosives should never be stored with: a) Cast boosters, b) detonating cord, c) non-electric or other blasting caps, d) All of the above.

Transportation

- Explosives and detonators must always be transported separately. (True/False)

- Never transport people or other materials in the cargo space along with blasting materials. (True /False)

- Only one warning sign is needed on vehicles transporting explosives True/ False

Handling And Use

- Modern explosives are safe enough to be handled by personnel without special training. True/FALSE

- If sensitive body areas are contacted by explosives material, they should be flushed with large quantities of water. True /False

- Only major roads leading to the blast site need guarding during a blast. True/ False

- The guarding of haulage roads into the blast area is limited to active haul roads only. True/ False

- Visual warning signals prior to a blast are an acceptable alternative to audible warning signals. True/ False

- Prearranged signals and timetables need only be posted. True/ False

Avoiding Flyrock Damage Or Injury

- Flyrock is a minor safety concern during blasting. True/ False

- Keeping to the same blasting schedule from shot to shot minimizes flyrock damage. (True /False)

Post Blast

- Deteriorated or damaged explosives are not dangerous. True/ False

- Never reuse any explosive material packaging. True /False

- Never burn explosive materials packaging in a confined area. True /False

- Stay away from blast area until fumes, dusts or mists have subsided. Never breathe dusts or vapors from explosive materials. True /False

- Misfires in muck piles are of little danger to large equipment. True/ False

- Only an experienced competent person, knowledgeable of the blast design, locations and types of explosive materials, should handle misfires. True /False

Blasting Safety for non-blasters - Answers & Discussion

General Safety

- Undetonated explosives are easy for anyone to identify. True / False

- A written blasting plan is required for using explosives. True / False

Explosives Storage

- An explosives magazine may be located near which of the following? a) power lines, b) fuel storage areas, c) damp, moisture laden areas, d) heavily populated areas, e) None of the above.

- Explosive magazines should not be identifiable as such to the general public. (True/ False)

- Explosives should never be stored with: a) Cast boosters, b) detonating cord, c) non-electric or other blasting caps, d) All of the above.

Explosive storage area, magazines or bulk ANFO storage areas are clearly marked with signs stating  "danger explosives" and "no smoking." Powder magazines must not be within 300 feet of mine openings, occupied buildings or public roads, or any other designated road, to promote safety. However, if sufficiently barricaded and approved, magazines may be located less than 300 feet from roads. Magazines are kept locked when unattended.

Transportation

- Explosives and detonators must always be transported separately. (True/False)

- Never transport people or other materials in the cargo space along with blasting materials. (True /False)

- Only one warning sign is needed on vehicles transporting explosives True/ False

Vehicles carrying blasting materials are identified by a sign, usually diamond-shaped, which indicates the class type explosive being carried. (Class a or class b type explosives.) Explosives must be carried in vehicles specifically designed for transporting explosives.

Handling And Use

- Modern explosives are safe enough to be handled by personnel without special training. True/FALSE

- If sensitive body areas are contacted by explosives material, they should be flushed with large quantities of water. True /False

- Only major roads leading to the blast site need guarding during a blast. True/ False

- The guarding of haulage roads into the blast area is limited to active haul roads only. True/ False

- Visual warning signals prior to a blast are an acceptable alternative to audible warning signals. True/ False

- Prearranged signals and timetables need only be posted. True/ False

When blasting is being conducted at surface mines, a code of blasting signals shall be posted in one or more conspicuous places at the operation, and employees shall be required to familiarize themselves with the code and conform to it.

Example of surface blasting signals. (Signals given by a horn or siren)

Warning signal-- a one-minute series of long blasts five minutes prior to the blast signal.

Blast signal---- a series of short blasts one minute prior to the shot

All clear signal-- a prolonged blast following the inspection of the blast site.

Normally, the certified blaster and/or surface foreman block roads leading to the blast area.

Avoiding Flyrock Damage Or Injury

- Flyrock is a minor safety concern during blasting. True/ False

- Keeping to the same blasting schedule from shot to shot minimizes flyrock damage. (True /False)

Never attempt to watch a shot being fired, be alert to fly-rock or any other unplanned event during blasting. Persons have been killed by fly-rock as far as one half mile away.

Post Blast

- Deteriorated or damaged explosives are not dangerous. True/ False

- Never reuse any explosive material packaging. True /False

- Never burn explosive materials packaging in a confined area. True /False

- Stay away from blast area until fumes, dusts or mists have subsided. Never breathe dusts or vapors from explosive materials. True /False

- Misfires in muck piles are of little danger to large equipment. True/ False

Any time blasted rock is hauled from a mine site, there is a chance that un-detonated explosives are included. If undetonated explosives are found, notify a powder representative to dispose of them.

- Only an experienced competent person, knowledgeable of the blast design, locations and types of explosive materials, should handle misfires. True /False

Never burn, bury or dissolve in water any types of blasting materials. Always contact a powder company representative.