LOADERS, TRUCKS & TRANSPORTATION CONTROLS

- List 5 causes of mobile equipment accidents.

  - ___________________________________

  - ___________________________________

  - ___________________________________

  - ___________________________________

  - ___________________________________

- What is “adequate maintenance”?

____________________________________________________________________

- Which of the following items should Vehicle Operator Training include:

  - How to paint the vehicle

  - How to do a thorough pre-shift inspection

  - Exactly what to do and who to contact when vehicle defects are identified

  - What to do when an unusual noise is heard

  - What to do when vehicle operation feels different than usual

  - Instructions on how to use the various controls, practice and feedback on performance

  - Information from the operator’s manuals

  - Identification of hazards and correct operating procedures associated with each step in the typical work cycle

- List one criterion for identifying excessive speed.

_______________________________________________________________

- Give 3 examples of distraction that may result in an accident?

  - ___________________________________

  - ___________________________________

  - ___________________________________

- Give 5 examples of an inadequately-maintained road!

  - ___________________________________

  - ___________________________________

  - ___________________________________

  - ___________________________________

  - ___________________________________

- Name 3 types of traffic control signs:

  - ___________________________________

  - ___________________________________

  - ___________________________________

- List 2 things that would be included in improper road design.

  - ___________________________________

  - ___________________________________

- What is the recommended safe way to dump a load on top of a pile?

_______________________________________________________________

- What are the 2 main things a berm should do?

  - ___________________________________

  - ___________________________________

- List 3 precautions you could take to help ensure that a dump truck would not turn over while dumping.

  - ___________________________________

  - ___________________________________

  - ___________________________________

- What are the main causes of a loader overturning?

  - ___________________________________

  - ___________________________________

- What is the first thing you do when entering the area where a loader is working?

_______________________________________________________________

- Where should smaller vehicles not park?

_______________________________________________________________

- Where should larger vehicles not park?

_______________________________________________________________

LOADERS, TRUCKS & TRANSPORTATION CONTROLS

- List 5 causes of mobile equipment accidents.

  - Inadequate vehicle maintenance

  - Inadequate training

  - Excessive speed

  - Inadequate road maintenance (holes, humps, rocks, dust)

  - Inadequate traffic controls, signs, etc.

  - Poorly designed roads (steep grades, intersections on hills or blind curves, road not wide enough)

  - Inadequate berms

  - Dumping over edges

  - Dumping under powerlines

  - Dumping on unstable ground or on grades

  - Dumping consolidated material

  - Loader travel with bucket raised

  - Roads too narrow

- What is “adequate maintenance”?

Regular preventinve maintenance as recommended by the manufacturer & correction of all problems identified in a thorough pre-shift inspection by a correctly-trained operator

- Which of the following items should Vehicle Operator Training include:

All EXCEPT "a"

- List one criterion for identifying excessive speed.

  - Faster than posted speed

  - Too fast to  maintain complete control under the conditions (road surface, hills, curves, visibility, vehicle load/condition, etc.)

  - Too fast to stop within the unobstructed distance that is clearly visible

- Give 3 examples of distraction that may result in an accident?

  - Adjusting the radio

  - Smoking or eating

  - Phone use

  - Daydreaming or dozing off

  - Turning eyes from the road to look at something else (including signs)

- Give 5 examples of an inadequately-maintained road!

  - Excessive dust

  - Holes or washouts

  - Large rocks

  - Inadequate berms

  - Bumps

  - Muddy areas

  - Snow or slush on road

- Name 3 types of traffic control signs:

  - Information signs

  - Stop signs

  - Speed limit signs

  - Do not enter signs

  - Warnings of unusual hazardous conditions (mud, water, ice, steep grades, blind intersections, narrow road, sharp curves, traffic changing from right to left and back, merging overhead traffic lines)

- List 2 things that would be included in improper road design.

  - Free space between vehicle and road edge or another vehicle is less than ½ the vehicle width.

  - Blind intersections on hills or curves

- What is the recommended safe way to dump a load on top of a pile?

  - Dump back from the edge using a dozer to push the material over.

- What are the 2 main things a berm should do?

  - Mark the edge

  - Help operator steer back onto the road

Most berms in the nation’s mines are constructed of a soft material.  The first thing a tire does when it goes into this earth berm is to sink in. Tests have shown that, to stop a runaway vehicle, for an 85-ton capacity vehicle or less you would need a berm height of three times the axle height. For trucks larger than 85 ton, you’d have to have four times the axle height.  This means that for trucks larger than 85 ton, if the axle height were 6 feet, we’d need a 6 x 4 = 24-foot-high berm to stop a runaway truck. Such a berm would be about 48 feet wide at the base because of the angle of repose for earth berms. This shows how impractical it would be to provide berms that could stop runaway vehicles.

- List 3 precautions you could take to help ensure that a dump truck would not turn over while dumping.

  - Level surface

  - Solid ground

  - Tailgate open

  - Loose material being dumped

- What are the main causes of a loader overturning?

  - Moving with the bucket raised

  - Dumping on ground that isn’t level or stable

- What is the first thing you do when entering the area where a loader is working?

  - Get the operator’s permission before you enter and have the operator guide you as to where to park or stand

- Where should smaller vehicles not park?

  - In the blind area(s) of moving or parked vehicles

- Where should larger vehicles not park?

  - Where they cannot see smaller parked vehicles from the driver’s seat.