Lockout/Tagout Quiz

- Place numbers from 1 to 7 in the blanks indicating the correct order of steps to be taken in lockout/tagout!

___	Isolate equipment

___	Verify isolation

___	Control stored energy

___	Shut down equipment

___	Prepare for shutdown

___	Apply lockout/tagout devices

___	Removal of locks

- Lockout/Tagout is a system used to ensure that equipment you’ve isolated and de-energized to work on remains shut down. True___, False___

- In a tagout, a tag is placed on all primary and secondary energy sources. True___, False___

- You know the equipment is safe when the power has been shut down. True___, False___

- It’s a good idea to have a pre-job briefing with your co-workers before a lockout operation. True___, False___

- Locks should be removed only by the person who installed them. True___, False___

- Kinetic energy is energy an object has when it is in motion. True___, False___

- In preparing for a shutdown, gravity is not a concern. True___, False___

- Which of the following must an employee know before starting to work on a piece of equipment. a) types of energy to be controlled, b) magnitude of energy to be controlled, c) hazards of energy to be controlled, d) method and means to control the energy.

- Which of the following must be notified prior to equipment shutdown for repair? a) plant manager, b) supervisor, c) safety person, d) affected employees.

- Which of the following would be part of equipment isolation? a) closing valves, b) locking out feeders, c) turning off power, d) releasing hydraulic pressure, e) releasing steam pressure, f) blocking movement of parts, g) releasing spring tension.

- Locks are located at each: a) electric panel, b) switch, c) water valve, d) energy isolating device.

- Which of the following would be part of control of stored energy? a) closing valves, b) locking out feeders, c) turning off power, d) releasing hydraulic pressure, e) releasing steam pressure, f) blocking movement of parts, g) releasing spring tension.

- Verifying isolation involves: a) putting locks on the equipment, b) putting a tag on the equipment, c) attempting to turn the machine on.

Lockout/Tagout Quiz - Answers

- Place numbers from 1 to 7 in the blanks indicating the correct order of steps to be taken in lockout/tagout!

_3__	Isolate equipment

_6__	Verify isolation

_5__	Control stored energy

_2__	Shut down equipment

_1__	Prepare for shutdown

_4__	Apply lockout/tagout devices

_7__	Removal of locks

- Lockout/Tagout is a system used to ensure that equipment you’ve isolated and de-energized to work on remains shut down. True___, False___

- In a tagout, a tag is placed on all primary and secondary energy sources. True___, False___

- You know the equipment is safe when the power has been shut down. True___, False___

- It’s a good idea to have a pre-job briefing with your co-workers before a lockout operation. True___, False___

- Locks should be removed only by the person who installed them. True___, False___

- Kinetic energy is energy an object has when it is in motion. True___, False___

- In preparing for a shutdown, gravity is not a concern. True___, False___

- Which of the following must an employee know before starting to work on a piece of equipment. a) types of energy to be controlled, b) magnitude of energy to be controlled, c) hazards of energy to be controlled, d) method and means to control the energy.

- Which of the following must be notified prior to equipment shutdown for repair? a) plant manager, b) supervisor, c) safety person, d) affected employees.

- Which of the following would be part of equipment isolation? a) closing valves, b) locking out feeders, c) turning off power, d) releasing hydraulic pressure, e) releasing steam pressure, f) blocking movement of parts, g) releasing spring tension.

- Locks are located at each: a) electric panel, b) switch, c) water valve, d) energy isolating device.

- Which of the following would be part of control of stored energy? a) closing valves, b) locking out feeders, c) turning off power, d) releasing hydraulic pressure, e) releasing steam pressure, f) blocking movement of parts, g) releasing spring tension.

- Verifying isolation involves: a) putting locks on the equipment, b) putting a tag on the equipment, c) attempting to turn the machine on.