Operating Forklifts Safely

QUESTIONS

- Forks are dangerous to use when wear exceeds a) 1 %, b) 5 %, c) 10 %, d) 25 %.

- As the load's center of gravity moves out toward the end of the forks, a lighter forklift can handle it. T, F

- When lifting pallets, place the forks as near to the center as possible without tipping the load. T, F

- The load's center of gravity should be as near to the rear of the forks as possible and as near to the center between the forks as possible. T, F

- It is important to locate the load's center of gravity before lifting it. T, F

- The position of the center of gravity of the load depends on: a) placement of load, b) height of load, c) angle of the floor with respect to horizontal, d) weight of the forklift.

- The vertical stability line or line of action is an imaginary vertical line through the loads center of gravity. T, F

- A heavier load moves the load's center of gravity to: a) the front, b) the rear.

- When traveling the load should be kept a) as low as possible, b) as high as possible.

- If the forklift tips, jump out. T, F

- Rear wheel steering causes the a) back end, b) front end of the forklift to swing wide on turns.

- When ascending or descending a grade, always keep the heavy end of the forklift a) uphill, b) downhill.

- Never drive the forklift across slopes at an angle. T, F

- The steepness of the incline affects forklift stability. T, F

Operating Forklifts Safely

ANSWERS

- Forks are dangerous to use when wear exceeds a) 1 %, b) 5 %, c) 10 %, d) 25 %.

- As the load's center of gravity moves out toward the end of the forks, a lighter forklift can handle it. T, F

- When lifting pallets, place the forks as near to the center as possible without tipping the load. T, F

- The load's center of gravity should be as near to the rear of the forks as possible and as near to the center between the forks as possible. T, F

- It is important to locate the load's center of gravity before lifting it. T, F

- The position of the center of gravity of the load depends on: a) placement of load, b) height of load, c) angle of the floor with respect to horizontal, d) weight of the forklift.

- The vertical stability line or line of action is an imaginary vertical line through the loads center of gravity. T, F

- A heavier load moves the load's center of gravity to: a) the front, b) the rear.

- When traveling the load should be kept a) as low as possible, b) as high as possible.

- If the forklift tips, jump out. T, F

- Rear wheel steering causes the a) back end, b) front end of the forklift to swing wide on turns.

- When ascending or descending a grade, always keep the heavy end of the forklift a) uphill, b) downhill.

- Never drive the forklift across slopes at an angle. T, F

- The steepness of the incline affects forklift stability. T, F