Training Plans and Procedures Test

- Part 48 is the part of 30CFR dealing with metal, coal, gypsum and underground mining operations. T___, F___

- Part 46 deals with almost all surface nonmetal, non-gypsum, non-coal mines as well as cement plants. T___, F___.

- A part 48 training plan requires MSHA approval, but a part 46 plan is considered to be approved if it meets the standards requirements. T___, F___

- Part 48 training, other than task and site-specific hazard training, must be done by MSHA-certified instructors. T___, F___

- Part 46 training must be done by MSHA-certified instructors. T___, F___

- A competent person who provides part 46 training to miners must be approved by MSHA. T___, F___

- Part 46 task training must be done by a competent person. T___, F___. *

- A Part 46 training certificate must be signed by the person responsible for safety and health at the mine, while a part 48 certificate may be signed either by the MHSA-certified instructor or by the person responsible for safety and health at the mine. T___, F___

- 4 hours of part 46 new inexperienced miner training must be completed before the miner goes to work and the remaining 20 hours may include a brief review of first aid, respirator training where applicable, and practice under the supervision of the competent person listed in the mine’s training plan. T___, F___

- A Part 46 training plan must include the name of the competent person who will oversee “supervised practice of the assigned task”. T___, F___

- Part 46 requires new experienced miners to have 4 hours of training before working. T___, F___. *

- Annual refresher training is required a)___ within 1 year of completing new miner or new experienced miner training,  b)___ during the following year by the end of the same month the miner was hired or had his last annual refresher training, or c)___ as soon as the rest of the miners get annual refresher training.

- Under Part 46 new inexperienced miner training, a short review of first aid must be taught within 60 days of starting work. T___, F___.

- Under Part 46, a new inexperienced miner must have a full first aid and CPR course before he can work. T___, F___. *

- An on-road truck driver who loads his own truck with sand and gravel is considered a miner under Part 46 and needs comprehensive training. T___, F___.

- An on-road truck driver who only goes on mine property to have the mine operator load his truck with sand and gravel is considered a miner under Part 46 and needs comprehensive training. T___, F___.

- Part 46 specifies the entire list of subjects required for annual refresher training. T___, F___  *

- A truck driver who hauls sand and gravel from one location on mine property to another location on mine property needs comprehensive training under Part 46. T___, F___

- Before Part 46 training can commence, the training plan used must be posted for 2 weeks at a location where the miners can review its contents. T___, F___

- To become an experienced miner under Parts 46 and 48, the person must have received new miner training T___, F___, have 12 months of cumulative experience T___, F___, and have gained his/her 12 months experience within 3 years. T___, F___  *

- People who maintain and/or repair mining equipment at mine sites for “frequent” or “extended” periods do not need comprehensive training if the equipment is shut down and away from mining activities. T___, F___

- A miner transferred to another Part 46 mine owned by the same employer only needs site-specific hazard awareness training. T___, F___

- A contractor who has the mine operator perform the contractor’s Part 46 training need not have a training plan T___, F___

- A Part 46 training plan can cover only one mine. T___, F___

- A Part 46 training certificate can list the names of more than one trainee. T___, F___

- Annual refresher training can address both Part 46 and Part 48. T___, F___

- Training records should be available where they can be sent to the mine site immediately at the request of the MSHA inspector. T___, F___

- Construction workers not exposed to mine hazards need only receive site-specific hazard awareness training. T___, F____

- Independent contractors, who are miners under Part 46, must make available at the mine site, a copy of each miner’s training certificates for inspection. T___, F___.

- Miners are required to carry Part 46 training certificates.  T___, F___

Training Plans and Procedures Test - Answers & Discussion

- Part 48 is the part of 30CFR dealing with metal, coal, gypsum and underground mining operations. T___, F___

- Part 46 deals with almost all surface nonmetal, non-gypsum, non-coal mines as well as cement plants. T___, F___.

- A part 48 training plan requires MSHA approval, but a part 46 plan is considered to be approved if it meets the standards requirements. T___, F___

- Part 48 training, other than task and site-specific hazard training, must be done by MSHA-certified instructors. T___, F___

- Part 46 training must be done by MSHA-certified instructors. T___, F___
Part 46 training for each subject covered must be done by the competent company person(s) and/or training organizations listed for that subject in the company’s training plan.

- A competent person who provides part 46 training to miners must be approved by MSHA. T___, F___

- Part 46 task training must be done by a competent person. T___, F___. 
The training organizations name (a mine is not a training organization), or a miner who is competent to train the subject matter must be listed in the mine’s plan.

- A Part 46 training certificate must be signed by the person responsible for safety and health at the mine, while a part 48 certificate may be signed either by the MHSA-certified instructor or by the person responsible for safety and health at the mine. T___, F___

- 4 hours of part 46 new inexperienced miner training must be completed before the miner goes to work and the remaining 20 hours may include a brief review of first aid, respirator training where applicable, and practice under the supervision of the competent person listed in the mine’s training plan. T___, F___

- A Part 46 training plan must include the name of the competent person who will oversee “supervised practice of the assigned task”. T___, F___

- Part 46 requires new experienced miners to have 4 hours of training before working. T___, F___.
Times must equal or exceed the minimum times listed in the mine’s training plan.

- Annual refresher training is required a)___ within 1 year of completing new miner or new experienced miner training,  b)___ during the following year by the end of the same month the miner was hired or had his last annual refresher training, or c)___ as soon as the rest of the miners get annual refresher training.

- Under Part 46 new inexperienced miner training, a short review of first aid must be taught within 60 days of starting work. T___, F___.

- Under Part 46, a new inexperienced miner must have a full first aid and CPR course before he can work. T___, F___. 
Advanced first aid, as required by 56.18010, must be offered to all interested miners and at least one trained person must be available at the worksite whenever work is taking place.

- An on-road truck driver who loads his own truck with sand and gravel is considered a miner under Part 46 and needs comprehensive training. T___, F___.

- An on-road truck driver who only goes on mine property to have the mine operator load his truck with sand and gravel is considered a miner under Part 46 and needs comprehensive training. T___, F___.

- Part 46 specifies the entire list of subjects required for annual refresher training. T___, F___  
Advanced first aid, as required by 56.18010, must be offered to all interested miners and at least one trained person must be available at the worksite whenever work is taking place.

- A truck driver who hauls sand and gravel from one location on mine property to another location on mine property needs comprehensive training under Part 46. T___, F___

- Before Part 46 training can commence, the training plan used must be posted for 2 weeks at a location where the miners can review its contents. T___, F___

- To become an experienced miner under Parts 46 and 48, the person must have received new miner training T___, F___, have 12 months of cumulative experience T___, F___, and have gained his/her 12 months experience within 3 years. T___, F___  
(see the standard for exceptions for miners who were experienced miners before Oct. 2, 2000 for Part 46 and February 3, 1999 for Part 48).

- People who maintain and/or repair mining equipment at mine sites for “frequent” or “extended” periods do not need comprehensive training if the equipment is shut down and away from mining activities. T___, F___

- A miner transferred to another Part 46 mine owned by the same employer only needs site-specific hazard awareness training. T___, F___

- A contractor who has the mine operator perform the contractor’s Part 46 training need not have a training plan T___, F___

- A Part 46 training plan can cover only one mine. T___, F___

- A Part 46 training certificate can list the names of more than one trainee. T___, F___

- Annual refresher training can address both Part 46 and Part 48. T___, F___

- Training records should be available where they can be sent to the mine site immediately at the request of the MSHA inspector. T___, F___

- Construction workers not exposed to mine hazards need only receive site-specific hazard awareness training. T___, F____

- Independent contractors, who are miners under Part 46, must make available at the mine site, a copy of each miner’s training certificates for inspection. T___, F___.

- Miners are required to carry Part 46 training certificates.  T___, F___