## Slide 1
HAZARD ALERT:
Compressed
Gases
Hazards associated with compressed gases used in underground coal mines include:
Flammable/explosive gases (acetylene, propane, MAPP)
Fire/explosion accelerants (oxygen)
Suffocation (fuel gases, argon, carbon dioxide, nitrogen)
Extreme force / pressure vessels (broken valve, burst tank)
Best practices:
Secure tanks for storage and protect them from damage
Remove hoses and gages when not in use
Install caps and secure tanks prior to transporting
Secure gas hoses and attachments when not in use
Do not transport gas cylinders on mantrips
Only one set of tanks on a section
Do not leave unattended tanks inby last open crosscut
Must be trained and qualified to use compressed gases Maintain tanks, hoses, and accessories in safe operating condition